## Slide 1: NTC ECU Identification Fault Overview NTC 0x0B9
FDD: ES011A
Description:
This diagnostic is responsible for detecting incorrect ECU Id either on the primary or secondary ECU.
Diagnostic Overview:
The Dual ECU Identification Function shall indicate a negative result if either of the following conditions are true
Primary ECU Id is either 0 or 3
Secondary ECU Id is either 0 or 3
Primary ECU Id is same as Secondary ECU Id
Valid SecdryEcuId is not received in a specified time window
ECU Communication time out occurs when trying to communicate with the secondary ECU
Typical Fault Response:
  F3 Failure
Probable Sources (Most to Least Probable):
    Communication Time out
    Broken pins to read the ECU Id or either ECUs
    Same ECU Id for both ECUs (Pin connection mismatch)
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 
Bit | Cause
0 | Identical ECU Identification Fault
1 | Primary ECU Invalid Identifier Fault
2 | Secondary ECU Invalid Identifier Fault
3 | Primary ECU Identifier Not Read Fault
4 | Secondary ECU Identifier Not Read Fault
5 | Secondary Ecu Request Identifier Time Out Fault
6 | Ecu Communication Time Out Fault
7 | Unused

## Slide 2: Revision Log
Rev | Revision
 | Initial Release